## Slide 1: Network-attached Encryption Accelerators
ECE532 - Final Presentation (Group 7)
Chunyee Chu
Serdar Ozturk
Soheil Shahrouz​

## Slide 2: Agenda
Overview
Initial Proposed System
Mid-Project System
Problems Faced
Changes Made
Final System
Custom/Pre-built Blocks
Design Process
What we Learned

## Slide 3: Overview
Encrypt data network on FPGA at line rate
Motivation
  Software implementation has high latency (OS overhead and DDR latency)
  Non-deterministic latency
  Power inefficient
A network attached hardware accelerator
  Custom IP-cores handle network traffic
  No OS overhead
  No external memory
  Low energy consumption and deterministic latency

## Slide 4: Initial System

## Slide 5: Mid-Project System
Ethernet Port
TEMAC
Parser
Distributer
ARP
ICMP
UDP Depacketizer
DES
UDP Packetizer
Aggregator
Packet
Type
AXI-Stream
HLS Core
AXI-MM

## Slide 6: Problems Faced
Lots of required research beforehand
Partial reconfiguration
  Hard to debug code with partial reconfiguration
  Hard to integrate with the rest of the project without it being completed
  There are concerns of program correctness when using an AXI interface with partial reconfiguration
A member of our team left during the term.

## Slide 7: Changes Made
Partial reconfiguration was removed
  After a seperate mid-project demonstration, partial reconfiguration was removed
SD card introduction
  To replace Partial Reconfiguration, we introduced SD-card implementation to the project.

## Slide 8: Final System
Ethernet Port
TEMAC
Parser
Distributer
ARP
ICMP
UDP Packetizer
Aggregator
DES
UDP Depacketizer
AXI-Stream
HLS Core
AXI-MM
AES
DEMUX
MUX
SD Card
MUX
DEMUX
SD Card
Notes: Integration of all blocks successfully done
AES and DES encryption meeting line rate of 12.5MB/s

## Slide 9: Custom Blocks Pre-Built Blocks
AXI DMA
PmodSD IP
Tri-Mode MAC
AES encryption core (HLS)
DES encryption/decryption core (HLS)
Network Cores (ICMP, ARP, UDP)

## Slide 10: Design Process
Split the work into three parts, each member is responsible for a part:
Worked in parallel, with regular assistance in-between members.
Simulations were used to verify correctness before full implementation.
Network
Encryption cores
Partial Reconfig/ SD card

## Slide 11: What we learned
Planning is one of the most important steps of the design process. Plan for failure!
Working with HLS
  Start from simple C or C++ codes
  Optimization techniques in hardware, e.g. writing nested loops, merging loops, partitioning arrays, “unrolling” …
  The benefits of using HLS ⇒ Rapid development!
Techniques of debugging
The importance of communication
Knowledges about networks, encryption algorithms and partial reconfiguration

## Slide 12: Demo